## Slide 1: 先进封装与集成芯片 Advanced Package and Integrated Chips
Lecture 9 : SoC/Chiplet Interconnect
Instructor: Chixiao Chen, Ph. D

## Slide 2: Course Project
Option I: Presentation ( I guess most students would choose )
  Pick up one paper from the pool (https://365.kdocs.cn/l/cpbY4B34cUnj first come first served), send a email or told me in wechat group, I will updated the paper selection in time.
  If you want to pick a paper not listed, please send me an email to get granted.
  Slides and Presentation: Prepare a 15min slides to introduce the work and 3-5 min Q&A. Send the slides to the homework mail after presentation.
Option II: Project
  Complete a component (AXI-streaming controller+PCS, PHY-TX/RX pair, Clock Generation, ) design according to UCIe standard (not in a group)
  Report and Presentation: Prepare a 5 min introduction and send the design report (<10 pages A4) to the homework mail, NO need for slides, show your draft report during presentation is OK.
1st Deadline: Tell me your choice by 5.6 on class / mail / wechat.

## Slide 3: Overview
Review on SoC Interconnect
  Bus based on-chip communication
  Network-on-Chips (NoCs)
From SoC Peripherals to Chiplet Interconnect
  Case Studies
  How advanced packaging affects System Performance

## Slide 4: Communication-centric Design for SoC
SoC = System on Chip
For modern SoCs like a smart phone SoC, communication is the most critical aspects.
It affects performance, power, area (PPA) & time-to-market.

## Slide 5: On-Chip Interconnect: Physical and System View
Interconnect: communication infrastructure connecting all IPs together
Physical Implementation Interconnect: to avoid too many wires, we need to multiplex data over a group of shared wires

## Slide 6: Evolution of on-chip Interconnect
Bus is the most simplest and widely used SoC Interconnect.
Bus definition: A collection of signals to which multiple IPs are connected

## Slide 7: Bus Terminology
Master: IPs tat initiates a read/write data transfer.
Slave: IPs that only responds to incoming transfer requests.
Arbiters: Control bus operation by selecting master to grant data transfers.
Bridge: Connects with different bus, acting as slave one side and master on other side.

## Slide 8: Bus signals
Address: transfer data’s source and destination, uniformed encoded for all on-chip IPs, driven by masters only
Data: real information sent and received by bus, can be shared or separated for read and write
Control: includes request and acknowledgements, specify different type of data transfer (R/W, burst, cacheable, byte mask, …)

## Slide 9: Basic Bus Circuit Implementation (Digital)
Historically tri-state drivers (high impedance to disconnect) is not friendly in recent CMOS digital circuit design.
Current bus implementation adopts differentiate Read & Write Data channels to replace tri-state drivers
Pipelining stage can be inserted to prevent long-distance transition and latency.

## Slide 10: Bus Transfer Modes
Single data transfer (w/o pipeline)
  first request to access bus
  access granted/acknowledged
  sent address and control signals
  send/receive data in subsequent cycles
Burst data transfer (w/i pipeline)
  send multiple data with only one cycle control ( save time for arbitration)
  Continuous data transfer for recent AI applications
There should be a protocol or standard for bus communication.

## Slide 11: AMBA Bus Protocol
Advanced Microcontroller Bus Architecture, open standard but owned by ARM
AMBA 2: AHB Advanced High-performance Bus, AMB 3&4: AXI Advanced Extensible Interface

## Slide 12: Bus Topologies
Hierarchical shared bus for different clock SoCs
Fully/partially Crossbar matrix
Ring bus

## Slide 13: Networks-on-Chips (NoCs)
Network-on-chips is a packet switch based on-chip interconnection schemes designed by a layered methodology. “route-packets, not wires”
NoCs use packets to route data from the source to destination PE via a network fabric that consists of routers, as well as links.

## Slide 14: Packet and Flit
Each core sent messages/packets including information how data flows through routers in the NoC.
Phit (Physical control digit) is a unit of data that is transferred on a link.
Flit (flow control digit) is unit of switching.

## Slide 15: NoC Topologies
NoC is kind of an advanced bus, which is more friendly on scalable architectures.
Many NoC Topologies is used: 2D mesh, Torus, butterfly, fat-tree,…
2D Mesh: equivalent link length
Torus : Ring connection for nodes at the edges, long end-around link
Butterfly

## Slide 16: Routing: Packet-Switched Based Interconnect
Courtesy by Y. Thonnart, ISSCC 2021 Tutorial 8

## Slide 17: Routing & Packet Format
In 2D mesh NoC, Coordinates-based Routing is most commonly used
  Destination coordinates is located in header
  Comparison to Router coordinates for X-Y routing
Other methods includes indicate sequence of turning encoded in header flit
  “East East North Local” …

## Slide 18: Routing: Traffic and deadlock
Courtesy by Y. Thonnart, ISSCC 2021 Tutorial 8

## Slide 19: Transaction-based Interconnect
Memory access is another common type interconnect, which normally use transaction based interconnect.
Normally memory have specific protocols
Memory Request/Response have different/independent channels, therefore multiple request are allowed.
Memory Interconnect issues: coherence in multi-core architecture
AMBA 5: CHI ( Coherent Hub Interface)

## Slide 20: From Bus/NoC to Off-Chip Interconnect
Protocol Layer
Adpater
PHY Layer

## Slide 21: Transaction/Packet Based Interconnect
are naturally good protocol supporting inter-chiplet interconnect.

## Slide 22: Case Study: NoC Partition with Multiple Chiplets
Intel Sapphire Rapids
4xCPU die(15 core each die) + 2D Mesh NoC
MCM Direct Connection with EMIB

## Slide 23: Case Study: NoC Partition with Multiple Chiplets
Cea-Leti: IntACT-Active Interposer with 6 chiplets and 96 cores
3-layer of distributed interconnect: On-chiplet 2D Mesh, short distance (Synchronous NoC) and long distance (Asynchronous NoC).

## Slide 24: How advanced Packaging affects Interconnect?
Given a 1466 TFLOPS @ FP8 AI processor with 64MB on-chip weight buffer storage (similar to Nvidia L40S), Please estimate the overall token rate when it is deployed to complete a 7-billion LLAMA-2 model inference (FP8). Assumed the overall model is buffered in (a) a 48GB GDDR6 external DRAM, (b) 80GB HBM2e .

## Slide 25: How advanced Packaging affects Interconnect?
 | GDDR 6 – 48GB | HBM 2E – 80GB
Per Pin Data Rate | 16 Gbps | 3.2Gbps
Data Pin Count Per Bank | 32 | 1024
Per bank bandwidth | 64 GBps | 409.6 GBps
Bank Number | 12 | 6
Overall Memory Bandwidth | 864 GBps | ~2040 GBps (with little loss)